PTFE

P.T.F.E is the most popular of the fluropolymers.

P.T.F.E suffers high elastic deformity under load which reduces it's effectiveness for bearing applications. It can be filled however, to allow it to be used for more demanding applications. Filled P.T.F.E is not suitable for food contact and should be used where increased hardness, creep resistance, and a lower wear rate are needed.

PTFE PROPERTIES

Excellent in:

Weather resistance

Chemical resistance

Electrical insulation

Operating temperatures (from -260°C to 260°C)

Thermal stability

Other properties:

Approved for food use,

Low flammability

Low water absorption

Very low coefficient of friction

PTFE APPLICATIONS

• Gaskets

• Slide bearings

• Dough rollers

• Insulators

• Valve stem seals

• Valve seats

• Extrusion nozzles

• Electrical sleeving

• Bushes

• Pipe lining

• O-rings

• Chute liners